## Slide 1: High Temperature H2 Production and Energy Initiatives at UF Energy Park
State of the Union on Florida Energy, University of Florida, Gainesville FL, 3/23/2016

## Slide 2: Paths to Solar Fuel Production
Photons (hν)
Electricity (e-)
Thermal Energy (Uinternal = f(T))
Synthetic Fuels via
Process
Energy Input
Photobiological
Photoelectrochemical
Photocatalytic
Photosynthesis
Thermochemical
Electrolysis
H2
CO+H2
CO
H2O/CO2
+
+
CO2
H2O
CO2
H2O
CO+H2
CO+H2
Solar thermal processes inherently operate at high temperatures and utilize the entire solar spectrum, and as such provide a thermodynamically favorable path to solar fuels production.
Fischer-Tropsch
Methanation

## Slide 3: Solar Thermal Electricity Production
Images: http://www.brightsourceenergy.com/

## Slide 4: Thermochemical Fuel Production
Chemical Reactor/Receiver
H2O/CO2
H2/CO
O2
FT Reactor
Compression
Cracking
Liquid Fuels (diesel, kerosene, etc.)
H2O purification/
CO2 sequestration
Qsolar
Heliostat Array
Absorber
Solar Concentration
Image: http://www.brightsourceenergy.com/
High Temperature

## Slide 5: Thermochemical Dissociation of H2O/CO2
Qsolar
Chemical Reactor
H2O/CO2
H2/CO
O2
Direct Dissociation
H2O → H2 + 0.5O2
CO2 → CO + 0.5O2
Two-Step Redox Cycle
1) MO → MO1-δ + δ/2O2
2) MO1-δ + δH2O → MO + δH2
+Δ
-Δ
Two-Step Redox Cycle
Lower temperatures (>1673 K)
Inherent separation of product gases
Direct Dissociation
High temperatures (> 2500 K)
Rapid quenching or separation of products

## Slide 6: Solar Reactor Technology
2010 – First operable and cyclable solar reactor demonstrating complete redox cycle
Average efficiencies reported ~ 0.6%
Room for optimization in several areas
  Structural optimization
  Reactor optimization
  Material optimization
  Heat recuperation
porous ceria
Chueh, W. C, Steinfeld, A. et al., Science 2010, 330 (6012), 1797-1801.

## Slide 7: Solar Reactor
Reactor Front (water-cooled)
Reactor
D≈20cm
H≈20cm
CeO2
structure
Al2O3
insulation
Inconel Shell
Quartz Window
Inlet
Purge Gas (Ar)
Inlet
Outlet
Concentrated
Solar Radiation
1500 ° C
O2
O2
O2
900 ° C
H2O / CO2
CO
H2
H2
Syngas
(H2 / CO)
Reduction:
2. Oxidation:
Furler, P., Scheffe, J.R., Steinfeld , A., Energy & Fuels 2012, 26 (11), 7051–7059.

## Slide 8: Solar Simulator – U. Florida

## Slide 9: Reactor Prototype
Rear view
Front view
Schematic depiction : cross-sectional view and front view

## Slide 10
Reactive material
Reactor tubes
Centre tube ( gas outlet)
Gas inlet
Heated zone
Aperture
High temperature insulation layer 1
High temperature insulation layer 2
Microporous silica
1
2
3
6
5
4
7
8
9

## Slide 11: Solar Reforming
Solar energy utilization probably greater because of isothermal operation and no separation work
  TH = TL < 1200 K
  Qheat = 0
  Esep = 0
CeO2
CeO2-δ
CeO2-δ
CeO2
δH2O
TL
TL
δH2
pCH4
pH2O
Qred + δCH4
2δH2 + δCO
11

## Slide 12: Theoretical Efficiency
Peak at 1100 K because reduction reaction completed above this temperature
No heat recuperation
Further investigation of operating conditions necessary
  ni,CH4 = 0.1

## Slide 13: Acknowledgements
University of Florida
  Kent Warren
  Richard Carrillo
  Julie Reim
  Ben Greek
  Kelvin Randhir
  Prof. David Hahn
Funding Sources
  ARPA-E
  UF: College of Engineering and MAE